## Slide 1
Maine Codes & Preservation

## Slide 2
Maine Codes & Preservation
Copyright 2018
Created and narrated by R. Michael Pullen, A.I.A., LEED, Artifex A.E., Bangor, Maine
For the Historic Preservation Program, City of Portland, Maine
and the Maine Historic Preservation Commission, Augusta, Maine
This publication has been financed in part with Federal funds from the National Park Service, Department of the Interior. However, the contents and opinions do not necessarily reflect the views and policies of the Department of the Interior, nor does the mention of trade names or commercial products constitute endorsement or recommendation by the Department of the Interior. The Maine Historic Preservation Commission receives Federal financial assistance for identification and protection of historic properties. Under Title VI of the Civil Rights Act of 1964 and section 504 of the Rehabilitation Act of 1973, the U.S. Department of the Interior prohibits discrimination on the basis of race, color, national origin, or handicap in its federally assisted program. If you believe you have been discriminated against in any program, activity, or facility as described above, or if you desire further information, please write to:
Office of Equal Opportunity
National Park Service
1849 C Street, N.W.
Washington, D. C. 20240

## Slide 3
Maine Codes & Preservation
“ Rehabilitating historic buildings involves compliance with
code and regulatory requirements, including accessibility, building
and life safety, and seismic upgrades.”
Technical Preservation Services, Nat’l. Park Service

## Slide 4
Maine Codes & Preservation
Maine’s Uniform Code (MUBEC)
IEBC 2015 & Preservation
NFPA LSC 101 & Preservation
State & Federal Accessibility Acts
Preservation Challenges & Successes

## Slide 5: Maine’s Uniform Code
Maine Codes & Preservation
Prior to the 2010 adoption of the MUBEC, a “patchwork quilt” of codes existed, leading to unnecessary confusion, and extra time & costs for permitting.
Existing and historic buildings required a more flexible approach to compliance, than that offered by the IBC.
MUBEC applies to communities >4,000 in population, and others that choose to adopt either MUBEC, MUBC, or MUEC.
“There is a need to make historic preservation a policy priority by way of model codes, to facilitate adaptive reuse and alternate compliance methods for historic buildings”.

## Slide 6: features of the mubec
Maine Codes & Preservation
Current Codes & Standards:
International Building Code (IBC) 2015
International Residential Code (IRC) 2015
International Existing Building Code (IEBC) 2015
International Energy Conservation Code (IECC) 2009
ASHRAE Standards; 62.1-2007, 62.2-2007 and 90.1-2007
Maine Model Radon Standard ASTM 1465-06

## Slide 7: features of the mubec
Maine Codes & Preservation
MUBEC Board Duties/ Composition:
Adopt, amend & maintain the MUBEC
Resolve conflicts between ICC & NFPA Codes
Board members represent Code Officials, Architects, Builders, Energy & Structural professionals
Historic Preservation interests are represented on the Board

## Slide 8: Provisions for historic buildings
Maine Codes & Preservation
IEBC International Existing Building Code
IECC International Energy Conservation Code
NFPA LSC 101(Fire Code)
Americans with Disabilities Act (ADA)

## Slide 9: historic building defined
Maine Codes & Preservation
Listed or preliminarily determined to be eligible for listing in the National Register of Historic Places;
Determined by the Secretary of the US Dept. of the Interior to contribute to the historical significance of a registered historic district or a district preliminarily determined to qualify as a historic district;
Designated as historic under a state or local historic preservation program that is approved by the Dept. of the Interior.

## Slide 10: Provisions for historic buildings
Maine Codes & Preservation
IEBC International Existing Building Code

## Slide 11: Provisions for historic buildings
Maine Codes & Preservation
IEBC International Existing Building Code

## Slide 12: International existing building code (iebc)
Maine Codes & Preservation
Compliance Options
Prescriptive Method
Work Area Method
Performance Method

## Slide 13: International existing building code (iebc)
Maine Codes & Preservation
Levels of Alteration
Maintenance & Repairs
Alterations
Changes of Occupancy & Use
Additions, New Work

## Slide 14: International existing building code (iebc)
Maine Codes & Preservation
Historic Building Evaluations
Compliant Safety Features
Defining Code Deficiencies
Providing Equivalent Levels of Safety

## Slide 15: Provisions for historic buildings
Maine Codes & Preservation
NFPA Life Safety Code 101
Section 43.10 Historic Buildings
Evaluation on Historic Building required
Replacement of missing features permitted
Allowances for MOE, Door Swings, Transoms,
Stairway Enclosures and Rated Assemblies

## Slide 16: Role of maine’s hp commissions
Maine Codes & Preservation
Protect local Historic Resources.
Provide Reviews for COA.
Act as Liaisons for HP to Govt. and the Public.

## Slide 17: Key hp Ordinance terms
Maine Codes & Preservation
Minor Revisions
Maintenance
Character-Defining Features

## Slide 18: Preservation challenges
Maine Codes & Preservation
Changes in Occupancy & Use
Character-Defining Features
Accessibility
Means of Egress
Energy Upgrades
Rooftop Structures
7. Character-Defining Features
8. Maintenance

## Slide 19: Preservation challenges
Maine Codes & Preservation
Changes in Occupancy & Use
Assembly to Business Occupancy
Merrill Bank acquires theatre building and expands into the 1888 Vestry.

## Slide 20: Preservation challenges
Maine Codes & Preservation
Changes in Occupancy & Use

## Slide 21: Preservation challenges
Maine Codes & Preservation
Changes in Occupancy & Use

## Slide 22: Preservation challenges
Maine Codes & Preservation
Accessibility

## Slide 23: Preservation challenges
Maine Codes & Preservation
Accessibility

## Slide 24: Preservation challenges
Maine Codes & Preservation
Accessibility

## Slide 25: Preservation challenges
Maine Codes & Preservation
Means of Egress

## Slide 26: Preservation challenges
Maine Codes & Preservation
Means of Egress

## Slide 27: Preservation challenges
Maine Codes & Preservation
Energy Upgrades

## Slide 28: Preservation challenges
Maine Codes & Preservation
Energy Upgrades

## Slide 29: Strategies for rehabilitation
Maine Codes & Preservation
Improving Energy Efficiencies
in Historic Buildings
Identify & evaluate the historic features of
the building.
Conduct a building performance evaluation.
Retain or restore historic features designed
to save energy & increase comfort.
Determine the most cost effective energy-
saving strategies.
Develop a long-term energy efficiency plan.
Employ durable and repairable materials.
Make changes that are reversible and can
be monitored.
Control moisture, particularly in walls and
basements, and for unhealthy air quality.

## Slide 30: Preservation challenges
Maine Codes & Preservation
Rooftop Structures

## Slide 31: Preservation challenges
Maine Codes & Preservation
Character-Defining Features
“The removal of historic materials or alterations of features and spaces
that characterize a property shall be avoided.”

## Slide 32: Preservation challenges
Maine Codes & Preservation
Character-Defining Features
“The removal of historic materials or alterations of features and spaces
that characterize a property shall be avoided.”

## Slide 33: Preservation challenges
Maine Codes & Preservation
Character-Defining Features
“The removal of historic materials or alterations of features and spaces
that characterize a property shall be avoided.”

## Slide 34: Preservation challenges
Maine Codes & Preservation
Character-Defining Features
“The removal of historic materials or alterations of features and spaces
that characterize a property shall be avoided.”

## Slide 35: Preservation challenges
Maine Codes & Preservation
Windows

## Slide 36: Preservation challenges
Maine Codes & Preservation
Storefront Windows

## Slide 37: Preservation challenges
Maine Codes & Preservation
Cladding Materials

## Slide 38: Preservation challenges
Maine Codes & Preservation
Deferred Maintenance
“Maintenance and repair required….
…shall not permit such historic structure to fall into a state of disrepair….”

## Slide 39: Preservation successes
Maine Codes & Preservation
Maine tax credit rehabilitation projects have delivered $856M in Maine since 2008, requiring specialized trades.
Because of the durability of these historic buildings, they are outlasting their more contemporary counterparts.

## Slide 40: Sustainable Rehabilitation
Maine Codes & Preservation

## Slide 41: Sustainable Rehabilitation
Maine Codes & Preservation

## Slide 42
Maine Codes & Preservation
Maine Historic Preservation Commission : www.maine.gov/mhpc/
Maine Downtown Center : www.mdf.org
Maine Preservation : www.mainepreservation.org
National Trust for Historic Preservation : www.preservationnation.org
ME Bur. Of Codes & Standards : www.maine.gov/dps/bbcs